## Slide 1: Comparison between Dr. Mitchell’s pipeline and ours
Kun Wang, Yanzhe Xu (Josh)

## Slide 2: Pipeline differences 1 - Normalization difference
Dr. Mitchell:
Ours:
Difference 1:
Gray scale should be between [0, 255] But Dr. Mitchell code increase normalization to [0, 256]
Difference 2:
After Dr. Mitchell get 256 gray scale, he uses ‘uint8’ transfer 256 to 0. Which means brightness pixel turns to darkness pixel

## Slide 3: ROI comparison Example1 Rwh: slice 17, slice coordinate (x, y) = (161,126), dicom file: Ax_T2_FSE_INTER_IM-0001-0017.dcm
For some other gray scales, they increase 1 gray scale level

## Slide 4: ROI comparison Example2 Rwh: slice 17, slice coordinate (x, y) = (161,126), dicom file: EPI+C_IM-0003-0017.dcm
For some other gray scales, they increase 1 gray scale level

## Slide 5: Pipeline differences 2 – LBP Border effect LBP radius = 3
Why LBP Border effect matters?
8*8 ROI box
Box border points
Box border points,
LBP radius = 3, means with center of point, get points’ grayscale of circle with radius = 3.
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
All black outside 8x8 ROI box, which means grayscale are all 0, when we calculate LBP of border points, we cannot get correct LBP because of this 0 padding
Compare each LBP border point gray scale with center gray scale to get binary number:
if gray scale of border < center gray scale: 0
Otherwises, 1
For this point LBP: 000000000 000001111
First 9 numbers 0 are all in 0 padding area, which is not correct LBP. 0 padding results in huge artifact in LBP calculation

## Slide 6: Pipeline differences 2 – LBP Border Handling difference LBP radius = 1/3
Dr. Mitchell:
Ours:
Difference:
Dr. Mitchell only use original 8*8 box to process LBP features, but it cannot solve LBP border effect. We use extended box to process LBP features, which solve LBP border effect

## Slide 7: LBP border handling comparison Example Rwh: slice 17, slice coordinate (x, y) = (161,126), dicom file: Ax_T2_FSE_INTER_IM-0001-0017.dcm LBP radius = 1
Dr. Mitchell’s LBP: 8*8 box
Our LBP: extended 10*10 box
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
For this point in Dr. Mitechell’s LBP:
00000011
This is not correct
For this point in Our LBP:
11100011
This is correct LBP for this border point
After we get correct of 8*8 box points by using extended 10*10 box points , we will zoom back to 8*8 box

## Slide 8: Summary
1. we use correct method to normalize gray scale to [0, 255] and we got same image with original box. But Dr. Mitchell normalize gray scale to [0, 256] then he made brightness points to darkness points.
2. we use extended box for eliminating LBP border effects and our LBP calculation for border points of 8*8 box is correct, but Dr. Mitchell did not consider 0 padding condition and use wrong LBP for border points of 8*8 box to calculate LBP.